## Slide 1: Fall Detection System for Elderly - Detects sudden falls and sends alerts
SACKEY, Vladimir Kwesi
SAHYOUN, Caroline
VOWOTOR, Brian Selorm Kobla Fui
OFOSU, Yeboah Desmond
OMAN, Madalene Kaki
OHIPENI, Annabelle Padiki
DERY, Kuusofaa David
OFORI, David
OFORI, Emmanuel Lartey Mawu Leley
OGILO, Ernest Emuseri Yaw
GROUP 19

## Slide 2: Contents
Overview
Software Implementation
Hardware Setup
Demonstration
Part 01
Part 02
Part 03
Part 04
Part 05
Future improvements

## Slide 3: Overview
01

## Slide 4: Project Description
It is fall detection program for the elderly that sends alerts to a caregiver
Fall Detection
Simulated on Wokwi using ESP32 and MPU6050 sensors with an led and a resistor
Simulation
Uses Blynk IoT to send alerts anytime a fall is confirmed
IoT Integration

## Slide 5: Hardware Setup
02

## Slide 6: Components
01
Microcontroller board
ESP32
02
Gyroscope and accelerometer sensor
MPU6050
03
Audible alert
Buzzer
04
Visual alert
LED

## Slide 7: Wiring
ESP32 connected to MPU6050, buzzer, and LED
Connections
Powered by USB or battery
Power Supply
02
01
I2C(Inter-Integrated Circuit) for MPU6050, WiFi for Blynk
Communication
03

## Slide 8: Software Implementation
03

## Slide 9: Fall Detection Algorithm
Detect free fall using low acceleration and gyro values or recorded magnitude
Free Fall
Detect impact using high acceleration and gyro values
Impact Detection
Confirm fall by checking for lack of movement using set thresholds in the code
Stillness Check

## Slide 10: Blynk Integration
Connect to WiFi network
WiFi Connection
Connect to Blynk IoT platform using authentication token generated for the specific ESP 32
Blynk Setup
A fall detection alert is sent to caregiver via Blynk
Alert Notification

## Slide 11: Demonstration
04

## Slide 12: Test Cases
Free Fall
  Simulate free fall and check for impact detection
False Alarm
  Simulate movement after impact and check for false alarm to ensure that only genuine falls are sent to caregiver
Successful Alert
  If a fall is detected an alert is sent to the caregiver, a buzzer is triggered and the led light turns on.

## Slide 13: Results
Reliable fall detection with minimal false positives
Accuracy
Prompt alert notification to caregiver in real time
Responsiveness
Suitable for elderly fall monitoring in home environments
Practical Application

## Slide 14: FUTURE IMPROVEMENTS
05

## Slide 15: Future improvements
Machine learning models to learn user (elderly person’s ) patterns in movement to ensure accurate fall detection.
Connectivity with GPS systems to aid in location tracking in the event of a fall and stillness.
Serialization of the fall detection system for each elderly person to enable multi-user interfacing and multiple fall detection.
Manual override button or switch on device to override accidental buzzer and LED alerts when there is a false alarm.

## Slide 16: Thank You
GROUP 19